## Slide 1
13 | Ext alarm | 1 | Upper input board
14 | Level alarm | 2 | 
 | GND |  | 
 | 3V3 |  | 
15 | Triori prox in | 3 | 
2 | Brush prox in | 4 | 
0 | Hatch speed out | 12 | EM241
4 | Hatch retract out | 9 | 
21 | Hatch extend out | 10 | 
 | GND | 8 | 
16 | Skip alarm but in | 1
17 | Open but/sw in | 2
5 | Close but/sw in | 3
18 | Open limit sw in | 4
19 | Closed limit sw in | 5
 | GND | 
GND | 5V |  | 3V3 | 25 RX | 22 TX
5V | 5V
23 | Alarm rel out | 1 | Relays
26 | Motor enable out | 2 | 
27 | Elevator2 stop out | 3 | 
12 | Elevator1 stop out | 4 | 
23 | Alarm rel buzz out |  | 
 | GND |  | 
3V3 | GND
33 | Elev 1.A prox in | 1 | Lower input board
32 | Elev 1.B prox in | 2 | 
35 | Elev 2.B prox in | 3 | 
34 | Elev 2.A prox in | 4 | 
39 | Hall in A | 6 | Screw connectors
36 | Hall in B | 7 | 
 | GND | 8 | 
 | 3V3 | 9 | 
GND input screw
+5 VDC input screw
AZ-Delivery
ESP32S Dev Kit C V4
Cap level alarm switches:
  Blue: GND / AC
  Brown: +24VDC / AC
  Gray: input board 2-
  Black: GND
  Yellow: not connected
  Input board 2+ => +12VDC
Hatch junction box connections:
Red1: 3V3 Blue1: GND
Red2: Hall1 Blue2: Hall2
Red3: Closed Blue3: Open limit
limit sw switch
Elevator&triori prox sw (PNP):
  Black: Input board +
  Input board - => GND
  Brown: +12VDC
  Blue: GND
  Wenglor I30H009
Brush prox (NPN):
  Black: Input board –
  Brown: +12VDC, Blue: GND
  Input board + => +12VDC